## Slide 1: Multi Threshold Technique for High Speed and Low Power Consumption CMOS Circuits
Xiaoyu hu
Aanchal gupta

## Slide 2: Topics covered
Introduction
Methodology
Framework
New MTOF Flip Flop Design
Conclusion

## Slide 3: I. Introduction
Need for Low Power Design
Reasons for Power Dissipation in flip-flops
How to achieve it?
MTCMOS

## Slide 4: Need for Low Power Design
Limited battery capacity for handheld and portable devices.
Personal communication service devices requires more battery life and support high end data and signal processing– requires low power and high performance circuits
Saves energy
Miniaturization of the circuit design
Increases circuit/system reliability
Minimum heat dissipation
Main drawback of current flip flop designs is the high power consumption and high delay time
Notes: High delay is because of cross coupled feedback design—it reduces operation speed and an increase in power dissipation is incurred
Low vth trans in cross coupled latches (critical path) to increase the speed of operation, other trans are high vt to reduce leakage current

## Slide 5: Reasons for Power Dissipation in flip-flops
Dynamic power—due to charging/discharging of gate capacitances with a change in input voltage
  Pdynamic = Cload*V2DD*fclock
  Td = Cload*VDD/(k(VDD-Vth)2
      Reduce VDD and Vth
      Reducing VDD makes the speed of operation very sensitive to the threshold voltage of transistor.
      But leakage current varies exponentially with Vth
Short circuit power
Leakage power dissipation– Up to 40% of the total power dissipation
Notes: Solution:
Short circuit power  gating transistors
Dynamic Power  MTCMOS

## Slide 6: How to achieve it?
Reduce supply voltage.
Reducing supply voltage degrades the speed of operation.
To support low power high speed operation we need to reduce the threshold voltage of the transistors
Reducing Vth increases threshold current exponentially  MTCMOS combines high Vth and low Vth
High Vth cuts off leakage current low Vth->reduces delay time, hence speed of operation is improved.

## Slide 7: MTCMOS
Disconnects the low Vth logic gates from the power supply and ground lines by cutting off the high Vt sleep transistors whenever the circuit is idle
Sequential circuits loose their state during the sleep mode. A low leakage sleep mode with data retention capability
High threshold transistors have intrinsically low leakage and does not require gating transistors

## Slide 8: II. Methodology
Power gating
Clock gating
Data retention circuitry
Simulation Setup
Block diagram

## Slide 9: Power Gating
Centralized power gating
  Advantageous considering the leakage paths are mutually exclusive
  Created virtual VDD and ground rails
Distributed power gating
  Simple to implement
  High area overhead
  Stack effect can degrade the performance
  More immune to ground bounce or voltage droop
Sleep control signal for maintaining and storing the circuit state during and after the sleep mode
The gating transistors are “on” during active mode and need to be wide enough to provide the required active current without significantly affecting performance.
Decide between fine and coarse granularity based on the circuit to avoid leakage paths
  If isolated circuitry is used for data storage—coarse granularity

## Slide 10: Clock Gating
Masks the clock signal when the circuit is not performing useful computation
Use an enable signal to control the clock signal during the sleep mode.

## Slide 11: Data Retention Circuitry
Reuse the part of the circuit used in the active mode to save the state during the sleep mode (improves performance as it avoids extra capacitive loads on the critical path)
Uses already existing control signals for controlling the data retention
Needs to maintain the state without increasing leakage during sleep or compromising performance during active mode.
Outer feedback

## Slide 12: Simulation Setup
Used NCSU PDK 45nm technology with VDD ranging from 0.8V to 1.1V
Input Buffer to make the simulation results more real
Clock gating
  Gclock = clkb nor sleep
Transistor sizing
  Gating transistors are sized 16x the minimum size transistor
  Transistors in the critical path are sized 4x the minimum size transistor
  Transistors not on the critical path are minimum sized

## Slide 13: Block Diagram
Fig. 1 Generalized block diagram

## Slide 14: III. Framework
Pseudo static MTCMOS with outer feedback
C2MOS Static MTCMOS Flip-flop
Master Side MTCMOS Flip-flop with OF
Conventional MTCMOS flip-flop with data preserving sleep mode
SRAM MTCMOS Flip-flop

## Slide 15: 1. Pseudo static MTCMOS with outer feedback
Fig.2(a) Circuit schematic of Pseudo-static MTCMOS FF with outer feedback
Notes: In active mode the outer feedback is off and the sleep gating transistors are all on. When entering sleep mode the sleep control signal is activated which disables all low threshold transistors, activates the outer feedback and
This completes a static latch with the outer feedback, the inner feedback inverters and the regular switch between the master and the slave. In this implementation the clock
needs to be kept low during the entire sleep period. It is important to note that the two nodes connected by the outer feedback (output of slave and input of master) always have the same logic value when the clock is low, hence closing the outer feedback involves no conflict or propagation delay. The circuit has a small area overhead (the outer feedback) and very little penalty in performance

## Slide 16: 1. Pseudo static MTCMOS with outer feedback
Key to this circuit is the outer feedback
  Off during the active mode and on during the sleep mode
  Forms a static storage loop with reused inner feedback circuits
  Data is stored on nodes connected with the critical path during sleep mode, thus there is no need to have complex data retrieving designs
Notes: In active mode the outer feedback is off and the sleep gating transistors are all on. When entering sleep mode the sleep control signal is activated which disables all low threshold transistors, activates the outer feedback and
This completes a static latch with the outer feedback, the inner feedback inverters and the regular switch between the master and the slave. In this implementation the clock
needs to be kept low during the entire sleep period. It is important to note that the two nodes connected by the outer feedback (output of slave and input of master) always have the same logic value when the clock is low, hence closing the outer feedback involves no conflict or propagation delay. The circuit has a small area overhead (the outer feedback) and very little penalty in performance

## Slide 17: 1. Pseudo static MTCMOS with outer feedback
Fig. 2(b) Simulation result of Pseudo-static MTCMOS FF with outer feedback
Notes: In active mode the outer feedback is off and the sleep gating transistors are all on. When entering sleep mode the sleep control signal is activated which disables all low threshold transistors, activates the outer feedback and
This completes a static latch with the outer feedback, the inner feedback inverters and the regular switch between the master and the slave. In this implementation the clock
needs to be kept low during the entire sleep period. It is important to note that the two nodes connected by the outer feedback (output of slave and input of master) always have the same logic value when the clock is low, hence closing the outer feedback involves no conflict or propagation delay. The circuit has a small area overhead (the outer feedback) and very little penalty in performance

## Slide 18: 2. C2MOS Static MTCMOS Flip-flop
Fig. 3 (a) Circuit schematic of C2MOS static MTCMOS flip-flop
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 19: 2. C2MOS Static MTCMOS Flip-flop
Fig. 3 (b) Simulation result of C2MOS static MTCMOS flip-flop
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 20: 3. Master Side MTCMOS Flip-flop with OF
Fig. 4 (a) Circuit schematic of Master-side MTCMOS flip-flop with OF
Notes: Again the outer feedback needs to be inverting as the input and output of the master latch have complementary values.
Clock needs to be low during the sleep mode

## Slide 21: 3. Master Side MTCMOS Flip-flop with OF
Uses separate nodes for storing the state during the sleep mode.
Critical path isolated from the outer feedback loop.
Notes: Again the outer feedback needs to be inverting as the input and output of the master latch have complementary values.
Clock needs to be low during the sleep mode

## Slide 22: 3. Master Side MTCMOS Flip-flop with OF
Fig. 4 (b) Simulation result for Master-side MTCMOS flip-flop with OF
Notes: Again the outer feedback needs to be inverting as the input and output of the master latch have complementary values.
Clock needs to be low during the sleep mode

## Slide 23: 4. Conventional MTCMOS flip-flop with data preserving sleep mode
Fig. 5 (a) Circuit schematic of MTCMOS flip-flop with data preserving sleep mode

## Slide 24: 4. Conventional MTCMOS Flip-flop with Data Preserving Sleep Mode
Fig. 5 (b) Simulation result for MTCMOS flip-flop with data preserving sleep mode

## Slide 25: 5. SRAM MTCMOS Flip-flop
Fig. 6 (a) Circuit schematic for SRAM MTCMOS flip-flop with data retention cell

## Slide 26: 5. SRAM MTCMOS Flip-flop
Fig. 6 (b) Simulation result for SRAM MTCMOS flip-flop with data retention cell

## Slide 27: Metrics Analysis
Setup time, leakage power, and area
 | Setup time (ps) | Leakage power (DQ=00, W) | Area (nm)
1 | 12.0 | 3.597e-9 | 14580
2 | 16.3 | 2.681e-9 | 19980
3 | 30.4 | 34.21e-12 | 18090
4 | 3.0 | 19.91e-12 | 14310
5 | 1.0 | 9.515e-15 | 11610
Notes: Again the outer feedback needs to be inverting as the input and output of the master latch have complementary values.
Clock needs to be low during the sleep mode

## Slide 28: Metrics Analysis
Leakage current during sleep mode (DQ=00)
Fig. 7 (a) Leakage comparison for MTCMOS FFs when input-output condition = 00
Notes: Again the outer feedback needs to be inverting as the input and output of the master latch have complementary values.
Clock needs to be low during the sleep mode

## Slide 29: Metrics Analysis
Leakage current during sleep mode (DQ=01)
Fig. 7 (b) Leakage comparison for MTCMOS FFs when input-output condition = 01
Notes: Again the outer feedback needs to be inverting as the input and output of the master latch have complementary values.
Clock needs to be low during the sleep mode

## Slide 30: Metrics Analysis
Leakage current during sleep mode (DQ=10)
Fig. 7 (c) Leakage comparison for MTCMOS FFs when input-output condition = 10
Notes: Again the outer feedback needs to be inverting as the input and output of the master latch have complementary values.
Clock needs to be low during the sleep mode

## Slide 31: Metrics Analysis
Leakage current during sleep mode (DQ=11)
Fig. 7 (d) Leakage comparison for MTCMOS FFs when input-output condition = 11
Notes: Again the outer feedback needs to be inverting as the input and output of the master latch have complementary values.
Clock needs to be low during the sleep mode

## Slide 32: New MTOF Flip-flop Design
Rising-edge MTCMOS FF with Slave-side Outer Feedback Design 1
Rising-edge MTCMOS FF with Slave-side Outer Feedback Design 2
  Schematic
  Logic function simulation
  Metrics analysis

## Slide 33: Rising-edge MTCMOS FF with Slave-side OF Design 1
Fig. 8 (a) Circuit schematic of rising-edge MTOF FF design 1
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 34: Rising-edge MTCMOS FF with Slave-side OF Design 1
Fig. 8 (b) Circuit schematic of rising-edge MTOF FF design 1
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 35: Rising-edge MTCMOS FF with Slave-side OF Design 1
Fig. 8 (c) Setup time simulation for rising-edge MTOF FF design 1
Metrics analysis – setup time
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 36: Rising-edge MTCMOS FF with Slave-side OF Design 1
Fig. 8 (d) Setup time failure for rising-edge MTOF FF design 1
Metrics analysis – setup time
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 37: Rising-edge MTCMOS FF with Slave-side OF Design 1
Fig. 8 (e) Leakage comparison for rising-edge MTOF FF design 1
Metrics analysis – leakage
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 38: Rising-edge MTCMOS FF with Slave-side OF Design 2
Fig. 9 (a) Circuit schematic of rising-edge MTOF FF design 2
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 39: Rising-edge MTCMOS FF with Slave-side OF Design 2
Fig. 9 (b) Circuit schematic of rising-edge MTOF FF design 2
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 40: Rising-edge MTCMOS FF with Slave-side OF Design 2
Fig. 9 (c) Setup time simulation for rising-edge MTOF FF design 2
Metrics analysis – setup time
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 41: Rising-edge MTCMOS FF with Slave-side OF Design 1 & 2
Metrics analysis
 | Setup time (ps) | Clock to Q delay (ps) | Leakage power (DQ=00, W) | Area (nm)
Design 1 | 1.86 | 25.34 | 3.579e-9 | 12420
Design 2 | 12.74 | 52.68 | 3.584e-9 | 9720
Notes: two nodes connected by the outer feedback (the output of the slave and the input of the master) are now complementary, hence the need for an inverting outer feedback.

## Slide 42: Conclusion
Detailed analysis of five MTCMOS flip flops using data retention ability.
Designed two novel multi threshold CMOS flip flops with an outer feedback and data retention capability during sleep mode.
Analyzed the flip flop characteristics that includes setup time, estimated area, leakage current during sleep mode for different input-output conditions, and leakage current vs. VDD ranging from 0.8V to 1.1V.